Quote:

Originally posted by darkfenriz hi quasi it seems very nice, just take care to mje350's thermal and miller C imbalance. I think they should be nicely matched and very close to each other on the same heatsink. 39p caps 2% or better.

Thanks Darkfenriz. Yes your comments are well received. The 2 MJE350's should be on the same heatsink. The two 4R7 resistors are there to help reduce mismatches between these transistors. Your advise about the two 39pF capacitors is noted.

Quote:

Originally posted by demogorgon whoa.. and i almost understand how it works too..

whoa....me too. The main difference with this amp and som eothers is the tempreture compensation built into the constant current source of the second stage and the way the FETS are driven.

Quote:

Originally posted by Rudy The wirebridge between C12 and the output after the coil does not need to be there, probebly just a drawing error. Rudy

Yes, the high frequency load impedance will be more gradual and predictable if I remove the link.

Quote:

Originally posted by audioPT Off-Topic - Quasi, with software did you used?

I used a software package called sPlan.

Quote:

Originally posted by richie00boy D5 needs an additional normal diode in series with it to prevent output rail spikes due to reactive load from reaching up to the upper MOSFET gate and turning it on spuriously.

I read lots of good advice from you. Yes I will put diodes in series with both zeners.


Cheers